## Slide 1: Introduction to Synthesis March 2023
For this lecture, material from Lebanese International University has been used
Mohamad Attieh, Ali Ibrahim, and Adnan Harb
Contact: adnan.harb@liu.edu.lb

## Slide 2: Cadence® Digital Realization of the RTL-to-GDSII Flow
Design Specification
RTL Coding
Functional Simulation
Logic Synthesis
Logic Equivalency Checking
Floor Planning
Power Planning
CTS
Static Timing Analysis/
Optimization
Routing
Gate-Level Simulation
GDSII
Parasitic Extraction
Placement
Signal Integrity
IR-drop/Electromigration
Signoff-Checks
Notes: Activity | Cadence Tool
Functional Simulation | Xcelium™ Simulator
Coverage Analysis | Integrated Metrics Center
Logic Synthesis | Genus™ Synthesis Solution
Logic Equivalency checking | Conformal® Logic Equivalency Checker
ATPG Vector Generation | 
Gate-Level Simulation | Xcelium Simulator

## Slide 3: Lecture Outline
This lecture is organized as follows:
Part A: Includes a general explanation of the synthesis theory
Part B: Introduces the design rule constraints
Part C: Provides some tips on script preparation before the synthesis
Part D: Explains the synthesis steps using Genus tool
Part E: Presents the Design for Testability Process

## Slide 4: Part A: The Synthesis Theory

## Slide 5: The Synthesis Theory
Definition:
Logic Synthesis is the process of transforming Hardware Description Language (HDL) code into a logic circuit based on:
a standard-cell library
user-specified optimization/timing constraints.
“Source: Cadence Customer Training Course RTLtoGDSII, Version: 5.0”

## Slide 6: The Synthesis Theory
The Synthesis process consists of three main stages which are:
MAPPING
OPTIMIZATION
+
TRANSLATION
+
LOGIC SYNTHESIS
=
Translation is the first step of the logical synthesis where the RTL is converted to a general library netlist. During translation, the following operations are performed:
HDL syntax checking
Optimizes HDL
Conversion of HDL into functional Boolean equivalent
Mapping of the arithmetic, sequential, and combinational function
TRANSLATION

## Slide 7
During mapping, the tool maps the generic Boolean netlist generated from the translation step, into the available gates in the standard cell library. The Boolean functions are mapped into technology-specific primitive functions.
MAPPING
In the optimization step, the mapping are modified in order to meet specific design goals such as speed, area, and power consumption
OPTIMIZATION

## Slide 8: The Digital Design Flow
Physical Synthesis
Product requirement
Tape out
Physical Description
Behavioral/RTL description
RTL synthesis
Gate-level netlist
Compare
Compare
Front end
Back end
Compare

## Slide 9: The RTL Synthesis Flow
RTL functional verification
Simulation or Formal Verification
Scan insertion and RTL synthesis
Gate-level netlist
RTL behavioral description
RTL Synthesis (Logic synthesis)
Gate-level netlist
Simulation or Formal verification
Specification
ok
NO
NO
ok
Pre-layout STA and power analysis
Physical Synthesis
Library Data
Result
Design environment and constraints
ok
YES
Debug
NO
Yes
ok
Block A
Block B
Yes
No

## Slide 10: Logic Synthesis Environment
The following must be provided to synthesis tools:
  Design environment
  Design constraints
  Gate-level netlist
  Technology library
RTL code
Technology library
Gate-level netlist
Design environment
Synthesizer
Design constraints

## Slide 11: Design Environment
Specify those directly influence
  design synthesis and optimization results
External operating conditions (PVT) include
  manufacturing process
    worst case: setup-time violations
    best case: hold-time violations
  operating conditions: voltage and temperature
I/O port attributes contain
  drive strength of input port
  capacitive loading of output port
  design rule constraints: fanin, fanout
Statistical wire-load model provides a wire-load model for processing the pre-layout static timing analysis.

## Slide 12: Design Constraints
clock signal specification
  period, duty cycle
  transition time, skew
Delay specifications
  input delay, output delay
  maximum, minimum delay for combinational circuits
Timing exception
  false path: instruct the synthesis to ignore a particular path for timing optimization
  multicycle path: inform the synthesis tool regarding the number of clock cycles that a particular path requires to reach its endpoint
Path grouping: bundle together critical paths in calculating a cost function

## Slide 13: The Architecture of Logic Synthesis Tools
RTL source
Technology Library
Front end
Back end
Logic Optimization
Parsing
Technology-dependent synthesis
Elaboration
Analysis/Translation
Technology-independent synthesis
Optimized gate-level netlist

## Slide 14: Logic Synthesis Tools: Front end
Parsing phase
  checks the syntax of the source code
  creates internal components
Elaboration phase (to construct a complete description of the input circuit)
  connects the internal components
  unrolls loops
  expands generate-loops
  sets up parameters passing for tasks and functions
  and so on

## Slide 15: Logic Synthesis Tools: Back end
Analysis/translation prepares for technology-independent logic synthesis.
  managing the design hierarchy
  extracting finite-state machine (FSM)
  exploring resource sharing and so on.
Logic optimization creates a new gate network that computes the functions specified by a set of Boolean functions, one per primary output.
Netlist generation generates a gate-level netlist.

## Slide 16: Logic Optimization
Major concerns when synthesizing a logic gate network:
  functional metric: such as fan-in, fan-out, and others.
  non-functional metrics: such as area, power, and delay.
Two phases of logic synthesis:
  technology-independent logic optimization
  technology-dependent logic optimization
The process of translating from a technology-independent to a technology-dependent gate network is called library binding.

## Slide 17: Technology-Independent Logic Optimization
Technology-independent logic synthesis
  Simplification rewrites a single function in the network to the literals of that network.
  Restructuring the network creates new function nodes that can be used as common factors and collapses sections of the network into a single node.
  Restructuring delay changes the factorization of a subnetwork to reduce the number of function nodes through which delay-critical signal must pass.

## Slide 18: Technology-Independent Logic Optimization
An example of simplification could be by expressing the network with newly created functions and variables.
For example:
S = xyz + ab, and T = xyz + ac
the new function is denoted by F = xyz therefore:
S = F + ab
T = F + ac

## Slide 19: Technology-Independent Logic Optimization
An example of the restructuring the network is when the divisor of the logical function is replaced by a new literal.
For example:
S = xyz + xyw ab, let u = xy and v = z + w
then we will have:
S = uv + ab

## Slide 20: Technology-Independent Logic Optimization
An example of the restructuring delay is by factorization which take place following three different steps: 1) generating the common factors, 2) selecting the factors to be substituted in the network, and then 3) reconstructing the network with the new factors.
For example:
S = xyz + xyw + ab,
Can be factorized into:
S = xy(z+w) + ab

## Slide 21: Technology Mapping
A two-step approach
  The network is decomposed into nodes with no nodes more than k inputs, where k is determined by the fan-in of each LUT.
  The number of nodes is reduced by combining some of them taking into account the special features of LUTs.
t u
v w
u x y'
z'
g
f1
f3
f2
t u
v
z'
w u
x y'
g
f1
f
3
f2
Mapping to 4 LUTs
Mapping to only 3 LUTs

## Slide 22: Technology-Dependent Logic Optimization
This task involves selecting the most cost-effective combination of primitive logic elements from a given library to cover a Boolean network.
The optimization process aims to minimize both the area and delay of the system.

## Slide 23: Summary on the Synthesis-Tool Tasks
Synthesis tools at least perform the following critical tasks:
  Detect and eliminate redundant logic
  Detect combinational feedback loops
  Exploit don’t-care conditions
  Detect unused states
  Detect and collapse equivalent states
  Make state assignments
  Synthesize optimal, multilevel logic subject to constraints.

## Slide 24: The Physical Synthesis Flow
Gate-level netlist
ok
Back to logic synthesis
No
Back to logic synthesis
Tape out
Post-global routing timing analysis
Formal verification
(Scan vs. CT inserted)
Placement
Clock tree insertion
Global routing
Detailed routing
Post-layout timing analysis
Library Description
ok
Formal verification
(Scan vs. CT inserted)
Technology Constraints
Technology Parameters
Yes
No
Yes

## Slide 25: Importance of Physical Synthesis
These same challenges ripple back from block-level synthesis to “unit-level” synthesis environments run by individual logic designers, often resulting in almost no correlation between what an RTL designer sees at the unit level and what the physical design team sees in P&R.

## Slide 26: Importance of Physical Synthesis
As correlation from P&R to unit-level synthesis degrades, more and more iterations are required between unit-level synthesis, block-level synthesis, and P&R, adding yet more pressure to achieve a fast turnaround time of each of these tasks by keeping block sizes small. A new generation of synthesis tool is needed to close this SoC “design productivity gap” one that is:
  • Scalable and has the parallelism to handle a large volume of blocks
  • Tightly correlated to P&R
  • Capable of enabling unit-level physical synthesis with a full understanding of P&R at the block level
Cadence has developed a next-generation logical and physical synthesis tool, the GenusTM Synthesis Solution, that is architected from the ground up to comprehensively address the design productivity gap.

## Slide 27: Physical Design using GenusTM Synthesis tool
Physical synthesis tool delivers up to a 10X boost in RTL design productivity with up to 5X faster
The solution can scale its capacity to well beyond 10 million instances flat. It also delivers tight timing and wire length correlation to within 5% of the place and route.

## Slide 28: Physical Synthesis Flows
Modern synthesis tools like Genus offer three physical-related flows. They provide increasing accuracy in predicting the wire lengths.
The simple PLE flow uses technology information and cell areas from the LEF libraries instead of from the synthesis technology libraries. The PLE flow uses parasitic resistance and capacitance values from the LEF libraries or the capacitance tables (if available) when estimating the wire lengths.

## Slide 29: Physical Synthesis Flows
The Genus-Physical flow uses in addition a complete placement and considers congestion and legal placement as a cost function during the RTL-to-gates phase, to create a better netlist. This flow requires access to the Innovus Place & Route tool

## Slide 30: Physical Information Files
floorplan file
LEF libraries
DEF file
Innovus Database
Capacitance Table
Genus

## Slide 31: Part B: Design Rule Constraints

## Slide 32: Constraint Definition
Performs logic and gate-level synthesis and optimization on the design.
Optimization is controlled by user-specified constraints:
Obtain the smallest possible circuit
Fastest design
Any other design requirement
The constraints describe:
Goals for the optimization process
Force specified outputs to meet timing requirements
Value for components area and speed used during synthesis and optimization are obtained from manufacturer libraries.

## Slide 33: Major Design Rule Constraints
set_db min_capacitance
Maximum Transition Time Fanout Capacitance
set_db cell_degradation
Cell Degradation
Design Rule Constraints
set_db max_transition
set_db max_fanout
set_db max_capacitance
Minimum Capacitance

## Slide 34: Major Design Optimization Constraints
set_max_area
set_db lp_power_analysis_effort
set_db power_optimization_effort
set_db lp_power_unit nw
set_db leakage_power_effort
create _clock
set_input_delay
set_output_delay
Optimization constraints
Area
Power/Leakage
Speed
set_max_delay
set_min_delay

## Slide 35: Power vs Area
Power
  Power optimization is not enabled by default.
  Optimizes power constraints for leakage power and dynamic power set by the attributes
  max_leakage_power & max_dynamic_power.
Area
  smallest design that satisfies the timing constraint by default
  set_max_area
  logic in the non-critical paths is automatically downsized to save area
The design goal is defined by the user constraint

## Slide 36: Part C: Before your Start – Prepare your Script

## Slide 37: Scripting
Scripting is the most efficient way of automating the tasks that are performed with any tool.
To support scripting at both a basic and advanced level, Genus uses the standard scripting language, Tool Control Language (TCL).
In most cases, a Genus script consists of a series of Genus commands listed in a file, in the same format that is used interactively.

## Slide 38: Script Example
#-------------------------------------------------------------------------------
# Info and path setup
#-------------------------------------------------------------------------------
if {[file exists /proc/cpuinfo]} {
sh grep "model name" /proc/cpuinfo
sh grep "cpu MHz" /proc/cpuinfo
}
puts "Hostname : [info hostname]"
set DESIGN "clock_divider"
set DATE [clock format [clock seconds] -format "%b%d-%T"]
set OUTPUTS_PATH ./results
set REPORTS_PATH ./reports
set_db init_hdl_search_path ../rtl/
set_db lib_search_path ../pdk/
#-------------------------------------------------------------------------------
# General Attributes
#-------------------------------------------------------------------------------
set_db information_level 9
set_db lp_insert_clock_gating true
set_db hdl_language vhdl
set_db hdl_vhdl_read_version 1993
#---------------------------------------------------------------------------
#clock
#-------------------------------------------------------------------------------------
create_clock -name clk -period 10 -waveform {0 5} [get_ports "clk"]
set_clock_transition -rise 0.1 [get_clocks "clk"]
set_clock_transition -fall 0.1 [get_clocks "clk"]
set_clock_uncertainty 0.01 [get_ports "clk"]
set_input_delay -max 1.0 [get_ports "reset"] -clock [get_clocks "clk"]
set_output_delay -max 1.0 [get_ports "clock_out"] -clock [get_clocks "clk"]
#-------------------------------------------------------------------------------
# Read design
#-------------------------------------------------------------
read_hdl -vhdl clock_divider.vhd
elaborate ${DESIGN}
syn_gen
syn_map
syn_opt
write_hdl > results/clock_divider.vhd
write_hdl > clock_divider_netlist.v
write_sdc > clock_divider_sdc.sdc
syn_opt -physical
gui_show
#Power root attributes
#--------------------------------------------------------------------------------------------
set_db lp_power_analysis_effort high
set_db lp_power_unit mW
set_db power_optimization_effort medium
set_db leakage_power_effort low
#-------------------------------------------------------------------------------
# Library setup
#---------------------------------------------------------------------------
set_db library { ../pdk/xh018/diglibs/D_CELLS_JIHD/v4_1/liberty_LPMOS/v4_1_1/PVT_1_80V_range/D_CELLS_JIHD_LPMOS_slow_1_62V_125C.lib \
../pdk/xh018/diglibs/IO_CELLS_F3V/v2_1/liberty_UPF_LPMOS/v2_1_0/PVT_1_80V_3_30V_range/IO_CELLS_F3V_LPMOS_UPF_slow_1_62V_3_00V_125C.lib }
set_db lef_library { ../pdk/xh018/cadence/v8_0/techLEF/v8_0_1_1/xh018_xx51_HD_MET5_METMID.lef \
../pdk/xh018/diglibs/D_CELLS_JIHD/v4_1/LEF/v4_1_1/xh018_D_CELLS_JIHD.lef \
../pdk/xh018/diglibs/D_CELLS_JIHD/v4_1/LEF/v4_1_1/xh018_xx51_MET5_METMID_D_CELLS_JIHD_mprobe.lef \
../pdk/xh018/diglibs/IO_CELLS_F3V/v2_1/LEF/v2_1_1/xh018_xx51_MET5_METMID_IO_CELLS_F3V.lef \
../pdk/xh018/spram/XSPRAMLP_128X16_M8P/v4_0_2/xh018_1151_LPMOS_MET5_METMID/LEF/XSPRAMLP_128X16_M8P.lef }
set_db cap_table_file { ../pdk/xh018/cadence/v8_0/capTbl/v8_0_1/xh018_xx51_MET5_METMID_typ.capTbl }
#___________________________________________________________________________________________

## Slide 39: Strategy For The Script
Path and information
General Attribute
Power Attribute
Library attribute
Clock
Set search path and timing library
Export Design
Apply constraints
Analyze
Perform Elaboration
Load HDL files
Synthesis

## Slide 40: Information and Path Setup
First, give the location for the code as the above figure
set_db init_hdl_search <destination>
Then search for the library path
set_db lib_search_path <destination>

## Slide 41: General Attribute
Define how detailed information you want to see in the terminal or
log files (normally you may have enough information by 5 to 7):
set_db information_level 9
Controls whether to generate clock-gating logic by using basic libcells if no usable integrated clock-gating cells are available in the library
set_db lp_insert_clock_gating true

## Slide 42: General Attribute
Specifies the VHDL version to be used when reading VHDL designs
set_db hdl_vhdl_read_version 1993
If your design consists of just one type of HDL file in “Configuring the Environment – native parameters”, set your flow default hdl language:
(hdl_language {v2001 | v1995 | vhdl | sv} Default: v2001)
set_db hdl_language vhdl

## Slide 43: Power Attributes
Specify attributes for the power optimization

## Slide 44: Library Setup
Define the attributes which specify the various libraries and LEFs for following
the flow in the design: Notice that these libraries are to be used as the specific target library from the technology to which you decide to map
set_db library { ../LIB/lib1.lib \ ../LIB/lib2.lib} /
set_db lef_library { ../LEF/lef1.lef \ ../LEF/lef2.lef} /
Specify the cap tables:
  set_db cap_table_file capfile

## Slide 45: Setting Effort Levels Prior to Synthesis
You can change the default effort levels for synthesis by using attributes.
  Default effort is:
    Medium for generic.
    High for mapping and optimization.
    None for global.
  Use the option express to enable express flow for both logical and physical synthesis.
  The express flow enables early feasibility analysis with much faster runtimes and reasonable quality of results.
Generic Synthesis (syn_generic command) effort level | set_db syn_generic_effort <low¦medium¦high¦express>
The optimization effort for the mapping stage (syn_map command) | set_db syn_map_effort <low¦medium¦high¦express>
The optimization effort to use for incremental optimization (syn_opt command) | set_db syn_global_effort <none ¦ low ¦ medium ¦ high ¦ express>
To specify the global effort for all synthesis commands, use | set_db syn_global_effort <none ¦ low ¦ medium ¦ high ¦ express>
“Source: Cadence Customer Training Course RTLtoGDSII, Version: 5.0”
Notes: This page does not contain notes.

## Slide 46: Timing Constraints
To accurately set up timing constraints, you need to specify the following:
Clock
I/O Timing requirements
Combinational path delay requirements
Timing exceptions
Clocks: To define a clock command is used, and the create_generated_clock is used command is used to define an internally generated clock. A few specifications of the clock include clock source, clock period, duty cycle, clock name, etc.

## Slide 47: Building a Clock
Create a clock and divide by 2 generated clock example is given bellow
create_clock –name SYSCLK_NAME –period 2 -waveform {0 1} {get_ports SYSCLK}
create_generated_clock –name DIVIDE -source {get_ports SYSCLK} divide_by 2 {get_pinsFF1/Q}

## Slide 48: Clock commands
Specify clock signal

## Slide 49: Part D: Synthesize Your Design using Genus tool

## Slide 50: Inputs and Outputs of Genus Synthesis Solution
Inputs | Outputs
RTL: Verilog, VHDL, directives, pragmas, SystemVerilog | Optimized netlist
Constraints: .sdc | LEC dofile
Library: .lib or .ldb | ATPG, ScanDEF, and others
Power Intent: CPF, UPF/IEEE 1801 (Optional) | Constraints: .sdc
Physical: Captable, QRC Technology file, LEF, DEF (Optional) | Physical design input files
RTL
.SDC
.cpf / .upf
Tech LEF or Captable
or QRC
Libcells LEF, DEF
Genus Synthesis Solution
Logic Verification Using LEC Dofiles
.lib / .ldb
Optimized Netlist
.SDC
Physical Design Input Files
ScanDEF
ATPG
Required Inputs
Optional Inputs
Outputs
“Source: Cadence Customer Training Course RTLtoGDSII, Version: 5.0”
Notes: This page does not contain notes.

## Slide 51: Genus Synthesis Flow
Place-and-Route
Set technology library and initial setup (read_libs)
Use read_mmmc if running MMMC flow
Read HDL files
read_hdl ${RTL_LIST}
Elaborate the design
elaborate
Set timing and design constraints
read_sdc
If running MMMC flow, constraints are specified in MMMC file
Apply Optimization Directives
syn_generic <-physical>
syn_map <-physical>
syn_opt <-spatial>
Yes
Modify Optimization Directives
Constraints Meet?
No
Netlist/DB Handoff, SDC
Report and Analyze
Write Output Files
Initialize the design (init_design)
(Optional, only required if MMMC file is read)
Synthesis Steps
Checking the Results
Output Files
Optional Steps
“Source: Cadence Customer Training Course RTLtoGDSII, Version: 5.0”
Notes: This page does not contain notes.

## Slide 52: Part E: Design for Testability

## Slide 53: What Is DFT?
Design for Test (DFT) techniques provide measures to comprehensively test the manufactured device for quality and coverage.
Design for Testability (DFT) makes it possible to:
  Assure the detection of all faults in a circuit.
  Reduce the cost and time associated with test development.
  Reduce the execution time of performing a test on fabricated chips.
Different faults in DFT:
  Stuck-At faults
  Transition faults
  Stuck open and Shorts
  Bridging faults
“Source: Cadence Customer Training Course RTLtoGDSII, Version: 5.0”
Notes: This page does not contain notes.

## Slide 54: Design with Test Circuit
clock
data_in
data_out
shift_enable
scan_in
scan_out
“Source: Cadence Customer Training Course RTLtoGDSII, Version: 5.0”
Notes: Any inferred register, or any instantiated edge-triggered registers that pass the DFT rule checks, are mapped to their scan equivalent cell when the scan connection engine runs.
Remapping of instantiated edge-triggered registers that pass the DFT rule checks to their scan equivalent cells occurs prior to placement only.
The test process refers to testing the ASIC for manufacturing defects on the automatic test equipment (ATE). It is the process of analyzing the logic on the chip to detect logic faults. The test process puts the circuit into one of the three test modes:
Capture mode This is the part of the test process that analyzes the combinational logic on the chip. The registers act first as pseudo-primary inputs (using ATPG-generated test data) and then as pseudo-primary outputs (capturing the output of the combinational logic).
Scan-shift mode This is the part of the test process in which registers act as shift registers in a scan chain. Test vector data is shifted into the scan chain registers, and the captured data from capture mode are shifted out of the scan registers.
System mode This is the normal or intended operation of the circuit. Any logic dedicated for DFT purposes is not active in the system mode.

## Slide 55: RTL Top-Down DFT Flow
Read target libraries/MMMC file
Read HDL files
Elaborate design
Set timing and design constraints (If running MMMC flow, constraints are specified in MMMC file)
Apply Optimization Directives
Synthesize design and map to scan (syn_generic <–physical>, syn_map <–physical>)
Yes
Modify Optimization Directives
Constraints Meet?
Netlist/DB Handoff, SDC ScanDEF, ATPG, abstraction model
Run incremental optimization (syn_opt <–spatial>)
Analyze the design
Initialize the design (Optional, only required if MMMC file is read)
No
Shift enable
Test mode
Internal clocks as test clocks
DFT-controllable constraints
Abstract scan segments
Test point insertion
Shadow logic insertion
Scan chains
Number of scan chains
Length of scan chains
Control data lockup elements
Connect scan chains
Set up DFT configuration constraints and preview scan chains
Set up for DFT rule checker
Run DFT rule checker and report registers
Fix DFT violations
Add testability logic
Modify Constraints
General Steps
Checking the Results
Output Files
Optional Steps
DFT Steps
“Source: Cadence Customer Training Course RTLtoGDSII, Version: 5.0”
Notes: The Cadence Genus Synthesis Solution provides a full-scan DFT solution including the following:
  DFT rule checking
  DFT rule violation fixing
  Scan mapping during optimization
  Scan chain configuration and connection
The main DFT techniques available today are given below:
  Scan insertion
  Programmable Memory BIST insertion
  Logic BIST insertion
  Boundary scan insertion
  Scan compression
  At-Speed Test using On-Product Clock Generation Logic (OPCG)
Scan insertion is one of the most used DFT techniques to detect stuck-at faults.
Scan insertion replaces the flip-flops in the design with special flops that contain built-in logic targeted for testability. Scan logic lets you control and observe the sequential state of the design through the test pins during the test mode. This helps in generating a high quality and compact test pattern set for the design using an Automatic Test Pattern Generator (ATPG) tool.

## Slide 56: Modus Test Disciplines
Correct-by-design test structures using Genus™:
  Verify (and optionally enforce) compliance with test design rules.
  Full range of tests for all types of digital testing.
  Diagnostics for fault isolation, failure analysis, and process monitoring.
Test
Synthesis
Test
Analysis
Test Generation
Test Diagnostics
“Source: Cadence Customer Training Course RTLtoGDSII, Version: 5.0”
Notes: Modus Test software is a fully integrated suite of tools designed from the beginning to interact and work with each other. Modus Test tools have already proven their ability to handle the next generations of nanometer technology.
Modus Test tools have embedded in them our expertise and 30+ years of experience in all four of the disciplines of test, and is a complete tool suite supporting all four disciplines:
  Test Synthesis – The process of inserting test logic into a design to help to make it testable.
  Test Analysis – The process of identifying the test logic and verifying that it has been inserted and integrated correctly, and identifying any design characteristics that will create testing problems.
  Test Generation –The process of creating test vectors that are applied at the tester.
  Test Diagnostics – The process of working backward from failure miscompares to the probable cause, and to help in the production and yield management of semiconductor lines.
We will focus on the traditional ATPG disciplines of Test Analysis and Test Generation.

## Slide 57: Modus Test ATPG Flow
Build Model
Build Fault Model (Add Faults)
Build Test Mode
Verify Test Structures
Internal Scan, Boundary Scan,
MemoryBIST, etc.
Create and Commit Logic Tests
Scan, Logic, Transition, IDDQ,
Memory BIST, etc.
Fix
Violations
Write Vectors for Verification
and Manufacturing
Major Inputs/Outputs
Processing Steps
Verilog Libraries
Netlist
Xcelium™
SimVision™
Voltus™
Patterns to ATE
Prepare for ATPG
Run ATPG
“Source: Cadence Customer Training Course RTLtoGDSII, Version: 5.0”
Notes: This is the basic recommended Modus Test flow.